## Slide 1: Network Function Virtualization

## Slide 2: Agenda
Why NFV?
NFV works with SDN
Service function chain (SFC)
Open platform for NFV (OPNFV)
Virtual machine management with OpenStack
Virtual function management with OpenNF
High speed VNFs with SR-IOV

## Slide 3: Agenda
Why NFV?
NFV works with SDN
Service function chain (SFC)
Open platform for NFV (OPNFV)
Virtual machine management with OpenStack
Virtual function management with OpenNF
High speed VNFs with SR-IOV

## Slide 4: Current Networks
The network functions in current networks are deployed in hardware boxes
It is expensive to make any extension or add new services

## Slide 5: Current Network Functions
It is costly to make any change on a network
DPI
BRAS
If we want to add a new middlebox
Purchase a new hardware
Config the hardware
Connect the hardware to the network
Config the network
Test
Time consuming and costly

## Slide 6: Network Function Virtualization
Virtualize the network functions as software-based functions and running in a cloud
DPI
Virtualize the network function as a software
Running in a cloud
void main(){
……
With virtualization, we can add, modify, and migrate network functions easily

## Slide 7: Benefits of NFV
Flexibility to easily, rapidly dynamically provision and instantiate new services in various locations (i.e. no need for new equipment install)
Reduced time-to-market by minimizing the typical network operator cycle of innovation. More service differentiation & customization
Improved operational efficiency by taking advantage of the higher uniformity of the physical network platform and its homogeneity to other support platforms
Reduced equipment costs through equipment consolidation on high volume industry standard servers leveraging the economies of scale of the IT industry
Reduced operational costs: reduced power, reduced space, improved network monitoring

## Slide 8: Fields of Application (examples)
Application-level optimisation: CDNs, Cache Servers, Load Balancers, Application Accelerators
Mobile networks: HLR/HSS, MME, SGSN, GGSN/PDN-GW, Base Station, EPC
Home environment: home router, set-top-box
Security functions: Firewalls, intrusion detection/protection systems, virus scanners, spam protection
Tunnelling gateway elements: IPSec/SSL VPN gateways
Traffic analysis/forensics: DPI, QoE measurement
Traffic Monitoring, Service Assurance, SLA monitoring, Test and Diagnostics
NGN signalling: SBCs, IMS
Converged and network-wide functions: AAA servers, policy control and charging platforms
Switching elements: BNG, CG-NAT, routers

## Slide 9: Use Case 1: Virtualized Customer Premise Equipment (CPE)
The functions in home APs are moved to a cloud in an ISP
firewall
radio
DHCP
routing
NAT
Internet
Core router
Home network
ISP
vFirewall
radio
vDHCP
vRouting
vNAT
Internet
vCore router
Home network
ISP
Virtual Functions

## Slide 10: Use Case 2: Virtualized Evolved Packet Core (EPC)
The network components are virtualized as VNFs
Internet
User Equipment
EPC
PCRF
S-GW
P_GW
MME
Access Network
Internet
PCRF
S-GW
P_GW
MME
Cloud
VNFs

## Slide 11: Use Cases Ranked

## Slide 12: Agenda
Why NFV?
NFV works with SDN
Service function chain (SFC)
Open platform for NFV (OPNFV)
Virtual machine management with OpenStack
Virtual function management with OpenNF
High speed VNFs with SR-IOV

## Slide 13: Network functions (NFs)
Perform sophisticated stateful actions on packets/flows
Intrusion detection
system (IDS)
Caching proxy
WAN optimizer

## Slide 14: NFV works with SDN
NFV → dynamically allocate NF instances
SDN → dynamically reroute flows
Dynamic reallocation of packet processing
Intrusion detection
system (IDS)
Caching proxy
WAN optimizer
Xen/KVM

## Slide 15: Example: elastic NF scaling
Satisfy performance SLAs
Minimize operating costs
Accurately monitor traffic
CPU
Packet loss

## Slide 16: NFV v.s. SDN
 | NFV | SDN
Approach | Service/Function Abstraction | Networking Abstraction
Formalization | ETSI | ONF
Advantage | Promises to bring flexibility and cost reduction | Promises to bring unified programmable control and open interfaces
Protocol | Multiple control protocols (e.g. SNMP, NETCONF) | OpenFlow is de-facto standard
Applications run | Commodity servers and switches | Commodity servers for control plane and possibility for specialized hardware for data plane

## Slide 17: NFV v.s. Cloud v.s. SDN

## Slide 18: Agenda
Why NFV?
NFV works with SDN
Service function chain (SFC)
Open platform for NFV (OPNFV)
Virtual machine management with OpenStack
Virtual function management with OpenNF
High speed VNFs with SR-IOV

## Slide 19: SFC High Level Architecture
Service Function Chain:
  The intended set of abstract service functions that must be traversed by the classified packets and the order of traversal
  E.g. DPI followed by parental control
Service Function Path:
  The actual instances of services traversed or specific instantiation of a service chain
Classifier:
  Determines what traffic needs to be chained based on policy

## Slide 21
Notes: Encapsulate

## Slide 23: Agenda
Why NFV?
NFV works with SDN
Service function chain (SFC)
Open platform for NFV (OPNFV)
Virtual machine management with OpenStack
Virtual function management with OpenNF
High speed VNFs with SR-IOV

## Slide 24: NFV Architecture
Computing Hardware
Storage Hardware
Network Hardware
Virtual Computing
Virtual Storage
Virtual Network
Virtualization Layer
VNF 1
VNF 2
VNF 3
VNF n
VNF Manges
VNF Manges
VNF Manager(s)
NFV Orchestrator
Virtualized Infrastructure Manager (VIM
NFV Management and Orchestration (MANO)
Virtual Network Functions (VNFs)
Network Function Virtualization Infrastructure (NFVI)

## Slide 25: Introduction to OPNFV
OPNFV is a carrier-grade, integrated, open source platform to accelerate the introduction of new NFV products and services.
The goals of OPNFV
  Develop an integrated and tested open source platform
  Meet the needs of user community
  Contribute to and participate in relevant open source projects
  Establish an ecosystem for NFV solutions based on open standards and software

## Slide 26: ETSI NFV Architecture Framework
OPNFV primarily focuses on NFVI
Computing Hardware
Storage Hardware
Network Hardware
Virtual Computing
Virtual Storage
Virtual Network
Virtualization Layer
VNF 1
VNF 2
VNF 3
VNF n
VNF Manges
VNF Manges
VNF Manager(s)
NFV Orchestrator
Virtualized Infrastructure Manager (VIM
Virtual Network Functions (VNFs)
Network Function Virtualization Infrastructure (NFVI)
OPNFV Scope

## Slide 27: OPNFV Releases
Release | Version | Release Date
Gambia | 7.2 | 1/28/2019
Fraser | 6.2 | 6/29/2018
Euphrates | 5.1 | Mon, 12/18/2017
Danube | 3.0 | Mon, 7/17/2017
Colorado | 3.0 | Mon, 11/14/2016
Brahmaputra | 3.0 | Fri, 04/29/2016
Arno | SR1 | Thu, 10/01/2015

## Slide 28: OPNFV Overview
There are three scopes in OPNFV
Integrate open source projects for NFV
Provide tools to test the system performance
Add new features other than the feature provided by integrated Projects
Notes: DPDK = Intel data plane development kit, add text to describe the point

## Slide 29: OPNFV: Integration
OPNFV integrate open source projects
Notes: DPDK = Intel data plane development kit

## Slide 30: OPNFV: Testing
Functional Testing (Functest suites)
  VIM (Virtualized Infrastructure Manager)
  Controllers
  Features
  VNF
  Kubernetes
System Limitation Testing
  Bottlenecks testing for VMs
  Bottlenecks testing for Docker
Performance Testing
  Storage performance: StorPerf
  Network performance: VSPERF
Notes: OPNFV提供了很多工具來對整個NFV系統做testing, 包含VM資源管理系統(指openstack), SDN controller…等等在功能是否正常(Kubernetes是container的管理系統), 另一類的工具是用來測系統效能的,包含VM的執行速度, container的執行决度, 最後一類工具是測試儲存設備的速度, 以及網路的傳輸速度(頻寬)

## Slide 31: Agenda
Why NFV?
NFV works with SDN
Service function chain (SFC)
Open platform for NFV (OPNFV)
Virtual machine management with OpenStack
Virtual function management with OpenNF
High speed VNFs with SR-IOV

## Slide 32: OpenStack
OpenStack is one of the major part of OPNFV
Similar to OpenFlow, OpenStack relies on a controller to manage infrastructure and provide north-bond API for cloud users

## Slide 33: OpenStack Components
To implement services and associated libraries to provide massively scalable, on demand, self service access to compute resources, including bare metal, virtual machines, and containers.
OpenStack includes several projects
NOVA
OpenStack Neutron is an SDN networking project focused on delivering networking-as-a-service (NaaS) in virtual compute environments.
NEUTRON
Cinder is a Block Storage service for OpenStack. It virtualizes the management of block storage devices and provides end users with a self service API to request and consume those resources without requiring any knowledge of where their storage is actually deployed or on what type of device.
CINDER

## Slide 34: OpenStack Components
Glance image services include discovering, registering, and retrieving virtual machine images.
OpenStack includes several projects
GLANCE
Keystone is an OpenStack service that provides API client authentication, service discovery, and distributed multi-tenant authorization by implementing OpenStack’s Identity API
KEYSTONE
Swift is a highly available, distributed, eventually consistent object/blob store. Organizations can use Swift to store lots of data efficiently, safely, and cheaply.
SWIFT

## Slide 35: OpenStack Components
OpenStack includes several projects

## Slide 36: Nova: Computing Manager
Manages computing resources for VMs or containers
Hypervisor e.g. KVM
NOVA

## Slide 37: NOVA: Availability Zones
Zone 1: Fast CPU
Zone 2: Larger MEM
Zone 3: DPDK Enabled
We can aggregate compute nodes as available zones
We can specify which zone to launch the VMs
Notes: Add text

## Slide 38: NEUTRON: Network Manager
Manage packet forwarding and virtual networks
Network Interface card
Open vSwitch or Linus bridge
VMs or containers
Internet
NEUTRON

## Slide 39: NEUTRON: OVS v.s. Linux Bridge
There are two options in Neutron to connect to VMs: OVS and Linux bridge
OVS:
  Support OpenFlow
  Required by DPDK
  Difficult to install
Linux bridge
  Simple and easy to install
  Cannot support OpenFlow

## Slide 40: Neutron: Virtual Networks
Cloud Network
192.168.100.0/24
Private Subnet 2
10.1.1.0/24
Private Subnet 1
172.16.1.0/24
VM
172.16.1.3
10.1.1.4
vRouter
vRouter
Floating IP
192.168.100.123
VM
Clients can create their own subnets and connect them to a cloud network
Inter-subnets

## Slide 41: NEUTRON: Inter-subnet Communication
Host
Host 1
Host
However, long route and floating IP translation are overhead and make throughput drop
Compute node
VM
OVS
Compute node
VM
OVS
Network node
L3 Agent
V
V
172.16.1.3
10.1.1.4
Floating IP
192.168.100.123
iPerf
Client
iPerf
Server
Public Net: 140.96.102.0/24
Subnet 1: 172.16.1.0/24
Subnet 2: 10.1.1.0/24
192.168.100.123
Notes: 這張投影片對應到前一張, VM是運行在compute node, 而vRouter是運行在network node中,而network node和compute node可能是不同的實體電腦. 當VM要傳封包給不同虛擬網路的VM時,需經過vRouter所以封包會先送到network node,再送回compute node (紅色箭頭是封包傳輸的方向). 封包在經過vRouter時,會做floating IP的轉換(發送端把封包傳向public floating IP, vRouter要把這個public IP傳成destination的private IP,再傳到其虛擬網路中

## Slide 42: NEUTRON: Availability Zones
Nodes are grouped as availability zones for vRouters
L3 agents are deployed in each compute node to enable vRouter availability zones
Zone 1
Zone 2
vRouter
V
L3 Agent
Network node
Host
L3 Agent
Network node
Host
L3 Agent
Network node
Host
Notes: VM可以藉由設定其availability zone來指定此VM要被運行在那一台實體伺服器中, vRouter也是同樣的情況,我們可以藉由設定指定vRouter要運行在那一台實體機器之中.

## Slide 43: NEUTRON: Define Router Availability Zones
An administrator defines vRouter availability zones
We setup the attribute “availability_zone” in neutron.conf to define the availability zone
availability_zone = Zone-2
availability_zone = Zone-2
availability_zone = Zone-1
Administrator
Zone 1
Zone 2
L3 Agent
Network node
Host
L3 Agent
Network node
Host
L3 Agent
Network node
Host
Notes: 因為目前Openstack的GUI還不支援vRouter的availability zone,因此,我們只能修改neutron.conf來指定每台實體機器是屬於那一個availability zone.

## Slide 44: NEUTRON: vRouter Placement
Users can put VM and vRouter to the same availability zone for shorter latency
V
Zone 1
VM 1
OVS
L3 Agent
Compute node
Network node
Host
VM 2
OVS
L3 Agent
Compute node
Network node
Host
User
Notes: 因為VM和vRouter都可以藉由設定availability zone來指定要運行在那一台實體機器,因此,我們可以將彼此有傳輸需求的VM和vRouter放在同一台實體機器之中,可以大大地減少傳輸latency,因為封包被送到實體網路的傳輸速度遠比在同一台實體機器內的傳輸要慢得多

## Slide 45: OpenStack Nodes
Traditionally, different nodes are deployed in different physical machines (hosts)
Inter-subnet communication should go a network node  higher latency
We combine the functions of compute and network nodes
Compute node
Control node
Network node
OpenStack Controller
Running VMs
vRouter to connect VMs in different virtual subnets

## Slide 46: The Steps to Launch a VM
There are some steps to boot up a VM
I
I
I
I
Image DB
Register the image with the platform
VM Instance
Compute Node
Activate VNF instance in a compute node
Create Networks
VM Image
Prepare an Image for the VNF
Connect the VMs to the Networks

## Slide 47: Agenda
Why NFV?
NFV works with SDN
Service function chain (SFC)
Open platform for NFV (OPNFV)
Virtual machine management with OpenStack
Virtual function management with OpenNF
High speed VNFs with SR-IOV

## Slide 48: OpenNF: States in NF
Each NF includes several states
How to manage the state in controller?
Src IP = 140.109.21.50 | Deny
Dst port = 80 | Accept
http://www.youtube.com | Content
http://www.ncu.edu.tw | Content

## Slide 49: OpenNF: SLAs + cost + accuracy: What do we need?
Quickly move, copy, or share internal NF state alongside updates to network forwarding state
Guarantees: loss-free, order-preserving, …



…
1
2
3
…
Also applies to other scenarios

## Slide 50: OpenNF overview
NF State Manager
Flow Manager
OpenNF Controller
Control Application
move/copy/share state
export/import State

## Slide 51: OpenNF: State Movement
NF State Manager
Control Application
move (port=80, Bro1, Bro2)
get(per, port=80)
[Chunk1]
put (per, Chunk1)
del(per, port=80)
[Chunk2]
put (per, Chunk2)
forward(port=80, Bro2)
Flow Manager
Bro2
Bro1
Also provide copy and share

## Slide 52: Agenda
Why NFV?
NFV works with SDN
Service function chain (SFC)
Open platform for NFV (OPNFV)
Virtual machine management with OpenStack
Virtual function management with OpenNF
High speed VNFs with SR-IOV

## Slide 53: NFV Performance
Packets are copied between different memory spaces between kernel and user space. It results in high latency

## Slide 54: Data Path Development Kit (DPDK)
By pass host kernel space to reduce the memory copy latency
OVS is used to forward packets to VMs
Kernel Space
User Space
VM
VM
VM
NIC
Packet
OVS
Kernel Space
User Space
VM
VM
VM
NIC
Packet
OVS
Without DPDK, packets are processed by network stack in Kernel
With DPDK, packets can bypass kernel space
Notes: 左圖是傳統Openstack基本的配置, 封包進入NIC會先被送到Kernel space,因為OVS運行在Kernel之中, 然後OVS會根據packet head將packet forward到VM,而VM是運行在user space,所以封包會被從kernel space copy到user space,再送到VM. 過多的memory copy和os interrupt造成很高的latency. 因此右圖運用了DPDK的技術, OVS只運行在user space,且封包直接進入user space中, 繞過kernel space, 因此可以減少memory copy和os interrupt的次數, 減少latency

## Slide 55: Signal Root I/O Virtualization ( SR-IOV)
SR-IOV NIC includes a L2-switch, so it don’t need OVS to forward packets anymore
Packets further by-pass the user space of host to reduce latency
Kernel Space
User Space
VM
VM
VM
Packet
SR-IOV NIC
L2 switch
Notes: 再更進一步, SR-IOV是新的NIC技術,內建一個硬體switch可以做forwarding,所以完全不需要軟體OVS做forwarding的動作,因此可以繞過kernel space和user space,直接由NIC將封包送到VM中,可以更進一步減少NFV的latency