## Slide 1: Network Virtualization
Lecturer: Shan-Hsiang Shen

## Slide 2: About this Course
New network technologies: SDN, NFV, P4, Network Slicing
Introduce some flatforms for the new network technologies
Lecturer: Shan-Hsiang Shen
Email: sshen@csie.ntust.edu.tw
Room: TR-617
Time: Thu. 2,3,4

## Slide 3: About this Course
Textbook: no textbook
Website: http://moodle.ntust.edu.tw
Project proposal (20%)
Labs (20%)
Final presentation (30%)
Final report (30%)

## Slide 4: Project
Team work
  3~5 people per team
  Send me your team name and members by Oct. 8
Proposal
  About the topic your group want to work on

## Slide 5: Project
Final
  Make a oral presentation
  Hand in a final report

## Slide 6: Software-Defined Networking

## Slide 7
Recall: per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 8: Routing in Traditional Networks
How to deliver packets to another side of a network?

## Slide 9: Routing in Traditional Networks
Nodes exchange network conditions

## Slide 10: Routing in Traditional Networks
Nodes exchange network conditions
Pick up a route with less cost

## Slide 11: Traffic engineering: difficult traditional routing
Q: what if network operator wants u-to-z traffic to flow along uvwz, x-to-z traffic to flow xwyz?
A: need to define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
Link weights are only control “knobs”: wrong!
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 12: Traffic engineering: difficult
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 13: Traffic engineering: difficult
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route blue and red traffic differently?
A: can’t do it (with destination based forwarding, and LS, DV routing)
Networking 401
Notes: Note: implicit assumption here: destination based forwarding

## Slide 14: Centralized Solution
Data plane
Data plane
Control plane
Data plane
Controller
Policies
Control plane
Control plane
Openflow

## Slide 15
Generalized Forwarding and SDN
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each router contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions

## Slide 16: Analogy: mainframe to PC evolution*
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
* Slide courtesy: N. McKeown

## Slide 17
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding in hardware
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 18
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 19
SDN perspective: control applications
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SND controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 20: OpenFlow
Developed in Stanford
  Standardized by Open Networking Foundation (ONF)
  Current Version 1.4
    Version implemented by switch vendors: 1.3
Allows control of underlay + overlay
  Overlay switches: OpenVSwitch/Indigo-light
PC

## Slide 21: OpenFlow Switching
Controller
OpenFlow Switch
Flow
Table
Secure
Channel
PC
OpenFlow
Protocol
SSL
hw
sw
OpenFlow Switch specification

## Slide 22: Background: Switch Internals
Logical View of a Switch
Physical Architecture of a Switch
Switching
Fabric
Processor
ASIC
AISC
data plane
control plane
Network O.S.
ASIC
Applications
Applications

## Slide 23: Software Defined Networking
Southbound API: decouples the switch hardware from control function
  Data plane from control plane
Switch Operating System: exposes switch hardware primitives
Network O.S.
Applications
Applications
Applications
Southbound
API
SDN
Switch Operating System
Switch Hardware
Network O.S.
ASIC
Applications
Applications
Current Switch
Vertical stack
SDN Switch
Decoupled stack

## Slide 24: Implications Of SDN
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Global View
Programmatic
Control
Current Networking
SDN Enabled Environment
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications

## Slide 25: Implications Of SDN
Current Networking
SDN Enabled Environment
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Distributed protocols
  Each switch has a brain
  Hard to achieve optimal solution
Network configured indirectly
  Configure protocols
  Hope protocols converge
Global view of the network
  Applications can achieve optimal
Southbound API gives fine grained control over switch
  Network configured directly
  Allows automation
  Allows definition of new interfaces
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications

## Slide 26: How to Pick an SDN Environment
Network O.S.
Applications
Applications
Applications
Southbound
API
SDN
Switch Operating System
Switch Hardware
What is the Southbound AP!?
Is the switch hardware and OS closed?
Is the switch virtual or physical?
How easy is it to develop on for the
Controller platform?

## Slide 27: The SDN Stack
Controller
NOX
Slicing
Software
FlowVisor
FlowVisor
Console
27
Applications
LAVI
ENVI (GUI)
…
n-Casting
NetFPGA
Software
Ref. Switch
Broadcom
Ref. Switch
OpenWRT
PCEngine WiFi AP
Commercial Switches
OpenFlow
Switches
…
Monitoring/ debugging tools
oflops
oftrace
openseer
Open vSwitch
HP, IBM, NEC, Pronto, Juniper.. and many more
OpenDaylight
ONOS
FloodLight
Source: SDN Tutorial by B. Heller
Open Networking Summit, April 2012
Notes: There are components at different levels that work together in making it work

## Slide 28
Controller
PC
OpenFlow
Access Point
Server room
OpenFlow
OpenFlow
OpenFlow
OpenFlow-enabled
Commercial Switch
Flow
Table
Secure
Channel
Normal
Software
Normal
Datapath

## Slide 29: How SDN Works: OpenFlow
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch H.W
Switch O.S
Switch H.W
Switch O.S
OpenFlow
OpenFlow

## Slide 30: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
Flow table in a router (computed and distributed by controller) define router’s match+action rules

## Slide 31: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard(萬用字元)

## Slide 32: OpenFlow: Anatomy of a Flow Table Entry
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
L4
sport
L4
dport
Match
Action
Counter
Forward packet to zero or more ports
Encapsulate(封裝) and forward to controller
Send to normal processing pipeline
Modify Fields
When to delete the entry
VLAN
pcp
IP
ToS
Priority
Time-out
What order to process the rule
# of Packet/Bytes processed by the rule

## Slide 33
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
Examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward (block) all datagrams sent by host 128.119.1.1

## Slide 34
Destination-based layer 2 (switch) forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
port3
Examples
layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to output port 6
22:A7:23:
11:E1:02

## Slide 35: OpenFlow: Types of Messages
Asynchronous (Controller-to-Switch) 非同步
  Send-packet: to send packet out of a specific port on a switch
  Flow-mod: to add/delete/modify flows in the flow table
Asynchronous (initiated by the controller)
  Read-state: to collect statistics about flow table, ports and individual flows
  Features: sent by controller when a switch connects to find out the features supported by a switch
  Configuration(組態): to set and query configuration parameters in the switch
Asynchronous (initiated by the switch)
  Packet-in: for all packets that do not have a matching rule, this event is sent to controller
  Flow-removed: whenever a flow rule expires, the controller is sent a flow-removed message
  Port-status: whenever a port configuration or state changes, a message is sent to controller
  Error: error messages
Symmetric (can be sent in either direction without solicitation)
  Hello: at connection startup
  Echo: to indicate latency, bandwidth or liveliness of a controller-switch connection
  Vendor: for extensions (that can be included in later OpenFlow versions)

## Slide 36: Dimension of SDN Applications: Rule installation
Proactive(主動) Rules
Reactive Rules
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S

## Slide 37: Dimension of SDN Applications: Rule installation
Proactive Rules
Controller pre-installs flow table entries
  Zero flow setup time
Requires installation of rules for all possible traffic patterns
  Requires use of aggregate rules (Wildcards)
  Require foreknowledge of traffic patterns
  Waste flow table entries
Reactive Rules
First packet of each flow triggers rule insertion by the controller
  Each flow incurs flow setup time
  Controller is bottleneck
  Efficient use of flow tables

## Slide 38: Dimensions of SDN Applications: Granularity of Rules
Microflow
WildCards (aggregated rules)
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S

## Slide 39: Dimensions of SDN Applications: Granularity of Rules
Microflow
One flow table matches one flow
Uses CAM/hash-table
  10-20K per physical switch
Allows precisions
  Monitoring: gives counters for individual flows
  Access-Control: allow/deny individual flows
WildCards (aggregated rules)
One flow table entry matches a group of flow
Uses TCAM
  5000~4K per physical switch
Allows scale
  Minimizes overhead by grouping flows

## Slide 40: Dimensions of SDN Applications: Granularity of Rules
Distributed Controller
Centralized Controller
Controller (N. O.S.)
Applications
Applications
Applications
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Controller (N. O.S.)
Applications
Applications
Applications
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Controller (N. O.S.)
Applications
Applications
Applications
Controller (N. O.S.)
Applications
Applications
Applications

## Slide 41: Google’ B4 Application
Rule installation
  Proactive
Rule Granularity
  Aggregate
Distributed
  Multiple instances

## Slide 42: OpenFlow: Message Formats
Controller encapsulates message into an object
  Accessor functions to different fields
  No need to worry about crafting network packets

## Slide 43: OpenFlow Actions (Partial list from OpenFlow 1.0 spec)
Output to switch port (Physical ports & virtual ports). Virtual ports include the following:
  ALL (all standard ports excluding the ingress port) - flood
  CONTROLLER (encapsulate and send the packet to controller) – PACKET_IN message
  LOCAL (switch’s stack) – go through the IP layer, etc (mostly used for vSwitches)
  NORMAL (process the packet using traditional non-OpenFlow pipeline of the switch) – traditional L2 forwarding, L3 routing
Drop
Set fields (packet modification/header rewriting)
  Ethernet Source address
  Ethernet Dest address
  IP source & dest addresses, IP ToS(type of service), IP ECN, IP TTL, VLAN
  TCP/UDP source and destination ports
Strip (pop) the outer VLAN tag
Set queue ID when outputting to a port (Enqueue)
New in OpenFlow 1.1+
  Support for matching across multiple tables
  Support for tunneling
  Support for Push/Pop mulitple VLAN/MPLS/PBB tags

## Slide 44: Flow Tables
There are two layers of flow tables

## Slide 45: Forwarding Delay
“Tango: Simplifying SDN Control with Automatic Switch Property Inference, Abstraction, and Optimization”, Aggelos Lazaris, Daniel Tahara, Xin Huang, Li Erran Li, Andreas Voellmy, Y. Richard Yang, and Minlan Yu, CoNEXT’14
Fast path delay: 0.665 ms
Slow path delay: 3.7 ms
Control path delay: 7.5 ms

## Slide 46: Topology Discovery
An OpenFlow controller discover topology by sending LLDP control messages
The controller discover the neighbor of a switch based on where packet-in comes from
Controller
Packet-out LLDP
Packet-in LLDP
Packet-in LLDP
Switch 1
Switch 2
Switch 3
Link Layer Discovery Protocol

## Slide 47: Host Tracking
Switch tells controller the host location when the host sends any data packet
Host location information
Data Packets