## Slide 1: P4: Protocol-Independent Packet Processors
Shan-Hsiang Shen
National Taiwan University of Science and Technology

## Slide 2: Agenda
The limitation of SDN
Why P4?
Packet processing in P4 architecture
Basic P4 programming
Table matching and action in P4
P4 + SDN: a more complete future network

## Slide 3: Agenda
The limitation of SDN
Why P4?
Packet processing in P4 architecture
Basic P4 programming
Table matching and action in P4
P4 + SDN: a more complete future network

## Slide 4: Network Slicing
To support multiple applications
Virtualization layer to support the slicing
Slice 1
Smartphones
Slice 2
Auto Driving
Slice 3
IoT
The virtualization layer may be attacked

## Slide 5: 5G Mobile Networks
SDN/NFV based networks
New network architecture encounters new security issues
PGW
SGW
MME
HSS
PCRF

## Slide 6: Software-Defined Networking
Network devices are divided into control and data planes
Data Plane
Control Plane
Controller
Remote Control Plane

## Slide 7: Software-Defined Networking
The controller install rules into forwarding table in switches to control traffic routing
Controller
Forwarding Table
headers counters actions

## Slide 8: The Limitation of SDN
The packet fields that can be matched are limited by OpenFlow protocol
The actions we can take on packets are also limited
OpenFlow switches reserve TCAM space for all possible fields  waste TCAM space

## Slide 9: Network Designs
A Bottom-up design V.S. a top-down design
Controller
Controller
A current SDN network (bottom-up)
A desired network (top-down)
What I can do
What you should do

## Slide 10: Agenda
The limitation of SDN
Why P4?
Packet processing in P4 architecture
Basic P4 programming
Table matching and action in P4
P4 + SDN: a more complete future network

## Slide 11: What is P4
P4 is a language to describe what a switch should do
SDN  programmable control plane
P4  programmable data plane
The goals:
  Reconfigurability
  Protocol-independence
  Target Independence
Controller
Programmable via SDN
Programmable via P4

## Slide 12: Benefits of Data Plane Programmability
New Features – Add new protocols
Reduce complexity – Remove unused protocols
Efficient use of resources – flexible use of tables
Greater visibility – New diagnostic techniques, telemetry, etc.
SW style development – rapid design cycle, fast innovation, fix data plane bugs in the field
You keep your own ideas
Think programming rather than protocols…

## Slide 13: Hardware for P4
new custom ASICs can achieve such flexibility at terabit speeds [Kangaroo INFOCOM ’10, SDN Chip SIGCOMM ’13, Intel FM6000 switch silicon]
some switches are more programmable than others:
  FPGA (Xilinx, Altera, Corsa)
  NPU (Ezchip, Netronome)
  CPU (OVS, …)

## Slide 14: Brief History
May 2013: Initial idea and the name “P4”
July 2014: First paper (SIGCOMM ACR)
Aug 2014: First P414 Draft Specification (v0.9.8)
Sep 2014: P414 Specification released (v1.0.0)
Jan 2015: P414 v1.0.1
Mar 2015: P414 v1.0.2
Nov 2016: P414 v1.0.3
May 2017: P414 v1.0.4
Apr 2016: P416 – first commits
Dec 2016: First P416 Draft Specification
May 2017: P416 Specification released

## Slide 15: Agenda
The limitation of SDN
Why P4?
Packet processing in P4 architecture
Basic P4 programming
Table matching and action in P4
P4 + SDN: a more complete future network

## Slide 16: Packet Processing in Switches
header
packet
Rule 1
Rule 2
Rule 3
Rule 4
Rule 5
Forwarding table
Forward
Drop
Fetch packet header
Match
Action

## Slide 17: Protocol-Independent Switch Architecture

## Slide 18: P4 Language Elements
Expressions
Data Types
Parsers
Controls
State machine, bitfield extraction
Tables, Actions, control flow statements
Basic operations and operators
Bistrings, headers, structures, arrays

## Slide 19: P416 Building Blocks
P4 Target: An embodiment of a specific hardware implementation
P4 Architecture: Provides an interface to program a target via some set of P4-programmable components, externs, fixed components
P416 Language
P416 Core Library
Extern Libraries
Architecture Definition

## Slide 20: P4 Target Programming
P4 Program
P4 Architecture Model
P4 Compiler
Target-Specific Configuration Binary
Tables
Extern Objects
Data Plane
CPU port
Control Plane
Add/remove table entries
Extern control
Packet-in/out
User supplied
Vender supplied
P4 runtime

## Slide 21: V1Model Architecture
Implemented on top of Bmv2’s simple_switch target
Match
Action
Match
Action
Match
Action
Match
Action
Traffic Manager
Match
Action
Match
Action
Match
Action
Match
Action
Parser
Ingress
Match-Action
Egress
Match-Action
Deparser
Packets
Metadata

## Slide 22: Agenda
The limitation of SDN
Why P4?
Packet processing in P4 architecture
Basic P4 programming
Table matching and action in P4
P4 + SDN: a more complete future network

## Slide 23: P416 Program Template (V1Model)
#include <core.p4>
#include <v1model.p4>
/* HEADERS */
struct metadata { ... }
struct headers {
ethernet_t ethernet;
ipv4_t ipv4;
}
/* PARSER */
parser MyParser(packet_in packet,
out headers hdr,
inout metadata meta,
inout standard_metadata_t smeta) {
...
}
/* CHECKSUM VERIFICATION */
control MyVerifyChecksum(in headers hdr,
inout metadata meta) {
...
}
/* INGRESS PROCESSING */
control MyIngress(inout headers hdr,
inout metadata meta,
inout standard_metadata_t std_meta) {
...
}
/* EGRESS PROCESSING */
control MyEgress(inout headers hdr,
inout metadata meta,
inout standard_metadata_t std_meta) {
...
}
/* CHECKSUM UPDATE */
control MyComputeChecksum(inout headers hdr,
inout metadata meta) {
...
}
/* DEPARSER */
control MyDeparser(inout headers hdr,
inout metadata meta) {
...
}
/* SWITCH */
V1Switch(
MyParser(),
MyVerifyChecksum(),
MyIngress(),
MyEgress(),
MyComputeChecksum(),
MyDeparser()
) main;
Parser
Ingress match-action
Deparser
Architecture description
Egress match-action

## Slide 24: V1Model Standard Metadata
ingress_port - the port on which the packet arrived
egress_spec - the port to which the packet should be sent to
egress_port - the port on which the packet is departing from (read only in egress pipeline)
struct standard_metadata_t {
bit<9> ingress_port;
bit<9> egress_spec;
bit<9> egress_port;
bit<32> clone_spec;
bit<32> instance_type;
bit<1> drop;
bit<16> recirculate_port;
bit<32> packet_length;
bit<32> enq_timestamp;
bit<19> enq_qdepth;
bit<32> deq_timedelta;
bit<19> deq_qdepth;
bit<48> ingress_global_timestamp;
bit<32> lf_field_list;
bit<16> mcast_grp;
bit<1> resubmit_flag;
bit<16> egress_rid;
bit<1> checksum_error;
}

## Slide 25: P416 Types (Basic and Header Types)
Basic Types
bit<n>: Unsigned integer (bitstring) of size n
bit is the same as bit<1>
int<n>: Signed integer of size n (>=2)
varbit<n>: Variable-length bitstring
Header Types: Ordered collection of members
Can contain bit<n>, int<n>, and varbit<n>
Byte-aligned
Can be valid or invalid
Provides several operations to test and set validity bit: isValid(), setValid(), and setInvalid()
Typedef: Alternative name for a type
typedef bit<48> macAddr_t;
typedef bit<32> ip4Addr_t;
header ethernet_t {
macAddr_t dstAddr;
macAddr_t srcAddr;
bit<16> etherType;
}
header ipv4_t {
bit<4> version;
bit<4> ihl;
bit<8> diffserv;
bit<16> totalLen;
bit<16> identification;
bit<3> flags;
bit<13> fragOffset;
bit<8> ttl;
bit<8> protocol;
bit<16> hdrChecksum;
ip4Addr_t srcAddr;
ip4Addr_t dstAddr;
}

## Slide 26: P416 Types (Other Types)
Other useful types
Struct: Unordered collection of members (with no alignment restrictions)
Header Stack: array of headers
Header Union: one of several headers
/* Architecture */
struct standard_metadata_t {
bit<9> ingress_port;
bit<9> egress_spec;
bit<9> egress_port;
bit<32> clone_spec;
bit<32> instance_type;
bit<1> drop;
bit<16> recirculate_port;
bit<32> packet_length;
...
}
/* User program */
struct metadata {
...
}
struct headers {
ethernet_t ethernet;
ipv4_t ipv4;
}

## Slide 27: P416 Parsers
Parsers are functions that map packets into headers and metadata, written in a state machine style
Every parser has three predefined states
  start
  accept
  reject
Other states may be defined by the programmer
In each state, execute zero or more statements, and then transition to another state (loops are OK)
MAC
VLAN
IP
TCP
start
accept
reject

## Slide 28: Parser Codes
/* From core.p4 */
extern packet_in {
void extract<T>(out T hdr);
void extract<T>(out T variableSizeHeader,
in bit<32> variableFieldSizeInBits);
T lookahead<T>();
void advance(in bit<32> sizeInBits);
bit<32> length();
}
/* User Program */
parser MyParser(packet_in packet,
out headers hdr,
inout metadata meta,
inout standard_metadata_t std_meta) {
state start {
packet.extract(hdr.ethernet);
transition accept;
}
}
MAC
VLAN
IP
TCP
Packet
Header
Metadata
Metadata
Standardmeta
Standardmeta
Extract packet header

## Slide 29: State Transition
P416 has a select statement that can be used to branch in a parser
Similar to case statements in C or Java, but without “fall-through behavior”—i.e., break statements are not needed
In parsers it is often necessary to branch based on some of the bits just parsed
For example, etherType determines the format of the rest of the packet
Match patterns can either be literals or simple computations such as masks
state start {
transition parse_ethernet;
}
state parse_ethernet {
packet.extract(hdr.ethernet);
transition select(hdr.ethernet.etherType) {
0x800: parse_ipv4;
default: accept;
}
}

## Slide 30: P416 Controls
Similar to C functions (without loops)
Can declare variables, create tables, instantiate externs, etc.
Functionality specified by code in apply statement
Represent all kinds of processing that are expressible as DAG:
  Match-Action Pipelines
  Deparsers
  Additional forms of packet processing (updating checksums)
Interfaces with other blocks are governed by user- and architecture-specified types (typically headers and metadata)

## Slide 31: P416 Controls: an Example (Reflector)
Very similar to C functions
Can be declared inside a control or globally
Parameters have type and direction
Variables can be instantiated inside
Many standard arithmetic and logical operations are supported
  +, -, *
  ~, &, |, ^, >>, <<
  ==, !=, >, >=, <, <=
  No division/modulo
Non-standard operations:
  Bit-slicing: [m:l] (works as l-value too)
  Bit Concatenation: ++
control MyIngress(inout headers hdr,
inout metadata meta,
inout standard_metadata_t std_meta) {
action swap_mac(inout bit<48> src,
inout bit<48> dst) {
bit<48> tmp = src;
src = dst;
dst = tmp;
}
apply {
swap_mac(hdr.ethernet.srcAddr,
hdr.ethernet.dstAddr);
std_meta.egress_spec = std_meta.ingress_port;
}
}

## Slide 32: Agenda
The limitation of SDN
Why P4?
Packet processing in P4 architecture
Basic P4 programming
Table matching and action in P4
P4 + SDN: a more complete future network

## Slide 33: Tables: Match-Action Processing
Key | Action ID | Action Data
Hit or Miss
Action code
Action data para.
Data Plane para.
Control Plane
Install rules
Headers and Metadata
Action ID
Data
Incoming Packet
Outgoing Packet

## Slide 34: Example: IPv4_LPM Table
Data Plane (P4) Program
  Defines the format of the table
    Key Fields
    Actions
    Action Data
  Performs the lookup
  Executes the chosen action
Control Plane (IP stack, Routing protocols)
  Populates table entries with specific information
    Based on the configuration
    Based on automatic discovery
    Based on protocol calculations
10.0.1.1
10.0.1.2
Key | Action | Action Data
10.0.1.1/32 | Ipv4_forward | dstAddr=00:00:00:00:01:01 port=1
10.0.1.2/32 | Drop | 
* | NoAction | 

## Slide 35: IPv4_LPM Table in P4 Code
table ipv4_lpm {
key = {
hdr.ipv4.dstAddr: lpm;
}
actions = {
ipv4_forward;
drop;
NoAction;
}
size = 1024;
default_action = NoAction();
}
/* core.p4 */
match_kind {
exact,
ternary,
lpm
}

## Slide 36: Defining Actions for L3 forwarding
Actions can have two different types of parameters
  Directional (from the Data Plane)
  Directionless (from the Control Plane)
Actions that are called directly:
  Only use directional parameters
Actions used in tables:
  Typically use directionless parameters
  May sometimes use directional parameters too
/* core.p4 */
action NoAction() {
}
/* basic.p4 */
action drop() {
mark_to_drop();
}
/* basic.p4 */
action ipv4_forward(macAddr_t dstAddr,
bit<9> port) {
...
}

## Slide 37: Applying Tables in Controls
control MyIngress(inout headers hdr,
inout metadata meta,
inout standard_metadata_t standard_metadata) {
table ipv4_lpm {
...
}
apply {
...
ipv4_lpm.apply();
...
}
}

## Slide 38: P416 Deparsing
Assembles the headers back into a well-formed packet
Expressed as a control function
  No need for another construct!
packet_out extern is defined in core.p4: emit(hdr): serializes header if it is valid
Advantages:
  Makes deparsing explicit...
but decouples from parsing
/* From core.p4 */
extern packet_out {
void emit<T>(in T hdr);
}
/* User Program */
control DeparserImpl(packet_out packet,
in headers hdr) {
apply {
...
packet.emit(hdr.ethernet);
...
}
}

## Slide 39: Agenda
The limitation of SDN
Why P4?
Packet processing in P4 architecture
Basic P4 programming
Table matching and action in P4
P4 + SDN: a more complete future network

## Slide 40: SDN + P4 as a Whole
P4 program configures forwarding behavior (abstract forwarding model)
express serial dependencies (e.g. ARP/L3 Routing)
P4 compiler translates into a target-specific representation
OF can still be used to install and query rules once forwarding model is defined
SDN Control Plane
Parser & table config.
Rule translator
Install and query rules
Config P4 program

## Slide 41: P4 Forwarding Model / Runtime
Parser
Match/Action Tables
Packet Meta
Egress Queues
L2L3.p4
Compile
SDN Control Plane
Routing
NAT

## Slide 42: Conclusion

## Slide 43: Conclusion