## Slide 1: Lab2: P4 + BMv2

## Slide 2: Installation
Download VM image from
  https://drive.google.com/uc?id=1lYF4NgFkYoRqtskdGTMxy3sXUV0jkMxo&export=download
Launch the VM
Copy the latest exercise
  git clone https://github.com/p4lang/tutorials

## Slide 3: Topology for Source Routing Exercise
H2
H1
H3
S1
S2
S3
1
2
2
3
2
3
1
1
3

## Slide 4: Homework 2
Modify P4 codes for source routing exercise
Use the “port” field in header “srcRoute_t” as a label for label routing
Modify the parser
Define to actions
  label_output: match the label and forward the packet to the port
  pop_label_output: remove header “srcRoute_t” and output to the port

## Slide 5: Homework 2
Create a table for label routing
Modify rules to forward the label “1” to h2
Run receive.py in h2
Run sender.py in h1
Handin:
  P4 codes: source_routing.p4
  Print the screen to show h2 receive data successfully
Deadline: Dec. 3 2020

## Slide 6: Homework 2
H2
H1
H3
S1
S2
S3
1
2
2
3
2
3
1
1
3
match | Action name | Action data
Label = 1 | label_output | 2
match | Action name | Action data
Label = 1 | pop_label_output | 1
Ethernet
Label=1, bos=1
IP
Ethernet
Label=1, bos=1
IP
Ethernet
IP